## Slide 1
Working with 3D graphs in the Si8000m and Si9000e PCB Transmission Line Field Solvers
Using the Sensitivity Analysis feature of the Si8000m and Si9000e Field Solvers to chart multiple parameter variations in controlled impedance structures
Application Note AP8171

## Slide 2: Sensitivity analysis in the Si8000m / Si9000e
© Polar Instruments 2009
<number>
The Si8000m and Si9000e series incorporate the Sensitivity Analysis tab to allow designers to plot the effects of varying parameters.

## Slide 3: Modeling varying parameters
© Polar Instruments 2009
<number>
<number>
In this presentation we use the 3D graphing facility of the Si8000m and Si9000e Field Solvers to illustrate the effect on impedance of varying parameters within a controlled impedance structure.
For this example we use the Si9000e to model the effect of simultaneously varying H1 and H2 of a two dielectric Offset Stripline structure 1B1A.

## Slide 4: Modeling varying parameters
© Polar Instruments 2009
<number>
Start the Si9000, click the Single-Ended Structures button and select the Offset Stripline 1B1A structure.
Click the Lossless Calculation tab and define the structure with the settings shown above.
Click Calculate – the resulting impedance should be around 50 Ohms.

## Slide 5: Modeling varying parameters
© Polar Instruments 2009
<number>
Note from the previous screen that the values of H1 and H2 were initially both set at 7 mil.
We’ll examine the effects on the impedance of the structure of increasing H1 from 4 to 10 mil while simultaneously decreasing H2 from 10 to 4 mil.
Sensitivity Analysis
Leave all the settings in the Lossless Calculation screen at their current values. The sensitivity analysis functions will use these values.
To switch to Sensitivity Analysis, click the Sensitivity Analysis tab.

## Slide 6: Modeling sensitivity analysis
© Polar Instruments 2009
<number>
On the Sensitivity Analysis screen note the two sections:
Impedance vs Changing Parameters – charts the change in impedance as a parameter (or parameters) change (in this example we will change H1 and H2)
Constant Impedance vs Changing Parameters – showing how the selected parameter must change to maintain a fixed impedance

## Slide 7: Modeling sensitivity analysis
© Polar Instruments 2009
<number>
In the Impedance vs Changing Parameters section:
Choose H1 as the first parameter and set its Range Start and Finish values to 4 and 10 mil respectively. Set the Increment value to 0.5
Choose H2 as the second parameter and its Range Start value to 10
Set its increment value to – 0.5 (i.e. to decrement as H1 is increasing)
From the Graph Settings set the Target Impedance to 50 Ohms
Click Calculate – you should see the graph below

## Slide 8: Modeling sensitivity analysis
© Polar Instruments 2009
<number>
The 2D chart plots the change in Z0 as H1 changes – we can view the data behind the chart by clicking the Results tab.
The sensitivity analysis function allows charting in 3 dimensions so we can plot the change in Z0 against the changes in both H1 and H2. With the Results tab selected it is possible to export this data to the the clipboard using the Edit|Copy Current Results tab to Clipboard option. Pasting the data into other tools (such as Excel) will facilitate further analysis.

## Slide 9: Using 3D graphing
© Polar Instruments 2009
<number>
To view the results graphically change the Graph Settings to 3D (leave the Target Impedance at 50 Ohms.) To improve clarity we change the H Increment to 0.1 and recalculate.

## Slide 10: Using 3D graphing
© Polar Instruments 2009
<number>
The chart now displays the change in Z0 against the changes in both H1 and H2. The chart can be rotated through 360° (double click the chart to stop and restart its rotation) – use the scroll bars to view the data from any angle

## Slide 11: Constant impedance v changing parameters
© Polar Instruments 2009
<number>
So far we have been viewing changes in Z0 against changing parameters.
Using the Constant Impedance vs Changing Parameters function we can plot a third parameter against a fixed impedance. Choose W1 against a target impedance of 50 Ohms. Click Calculate – the results are shown below.

## Slide 12: Constant impedance v changing parameters
© Polar Instruments 2009
<number>
The plot below illustrates how the Si8000 and Si9000 field solvers can provide powerful and rapid graphical analysis – in this case, the range of values of trace width for a constant impedance of 50 Ohms as a signal trace is offset within defined limits between the two reference planes.

## Slide 13: June 30 2009 Competition question
© Polar Instruments 2009
<number>
We noticed on slide 7 that although H1 sweeps through 4 to 10 mil and H2 from 10 to 4 mil, the resulting impedance Z0 begins at 46 Ohms but ends at 40.3 Ohms. Why does the impedance curve not appear symmetrical?
Solution: To achieve a more symmetrical curve we need to take into account both the thickness and the profile of the copper signal trace…
…see next slides…

## Slide 14: Solution to competition
© Polar Instruments 2009
<number>
1st order calculation:
  Total dielectric height in this example = 4 + 10 = 14 mil; the copper signal trace is 1.2 mil thick – (T1 =1.2)
  When dielectric heights are equal (H1 = H2) the copper will not be centred between the reference planes but embedded into H2
  So for this first order calculation imagine a line drawn horizontally through the centre of the signal trace; then to a first order approximation the point of symmetry will occur when H1 + ½T1 = H2 – ½T1 = 7 mil

## Slide 15: Solution to competition
© Polar Instruments 2009
<number>
For our example therefore we use:
  H1 – ½T1 (4 – 0.6 = 3.4) as the Range Start Value and 9.4 as the Range Finish Value, Increment by 0.5
  H2 + ½T1 (10 + 0.6 = 10.6) as the Start Value, Increment by –0.5
  The resulting graph is shown below

## Slide 16: Solution to competition
© Polar Instruments 2009
<number>
2nd order calculation:
  The signal trace is often not purely rectangular but trapezoidal (W1 > W2)
  For this example, let’s assume a rectangular trace and make W1 = W2 (So that we can goal seek on trace width for a 50 Ohm impedance, in the Si8000/Si9000 Configuration dialog we’ll set the Lower Trace Width Etch Factor Setting to 0)

## Slide 17: Solution to competition
© Polar Instruments 2009
<number>
Set Lower Trace Width Etch Factor Setting to 0
Now on the Lossless Calculation tab goal seek on Upper Trace Width for 50 Ohms…

## Slide 18: Solution to competition
© Polar Instruments 2009
<number>
Running the Sensitivity Analysis calculation again… Z0 now begins and ends at 43.39 Ohms.

## Slide 19: Transferring the solution to your own stack
© Polar Instruments 2009
<number>
The solution may be easily transferred to Speedstack Stackup Builder where you can use it to build a working stack with available materials, adjusting automatically for inverted structures and copper embedding and finishing.

## Slide 20: Summary
© Polar Instruments 2009
<number>
It is useful to understand how the structure parameters interact and within the Si8000m and Si9000e field solvers Sensitivity Analysis is a fast and visual technique to display that interaction. By graphing multiple calculations over user-specified parameter ranges Si8000m and Si9000e Sensitivity Analysis immediately reveals trends that are not easy to discover from a single result.
For further information on the range of Polar field solvers visit the Polar web site www.polarinstruments.com

## Slide 21
For more information:
Contact Polar now: Phone
USA / Canada / Mexico Ken Taylor ( 503) 356 5270
Asia / Pacific
Terence Chew +65 6873 7470
Japan
Terumitsu Tsuji +81 45 339 0155
UK / Europe Neil Chamberlain +44 23 9226 9113
Germany / Austria / Switzerland Hermann Reischer +43 7666 20041-0
www.polarinstruments.com