## Slide 1
Documenting low layer count impedance controlled stacks with Speedstack VMM
Professional documentation of low layer count stacks using Speedstack’s Virtual Material and Material Library modes

## Slide 2: Material Library and Virtual Material modes
Polar’s Speedstack provides the option for you to switch easily between its Material Library and Virtual Material modes allowing you to build and experiment with stackups.
This enables you, for example, to examine the effects on impedance structures of different trace widths or dielectric heights without requiring real materials to be entered into a materials library.
<number>
© Polar Instruments 2010

## Slide 3: Material Library and Virtual Material modes
In this presentation you’ll use both modes to build a low layer count stackup – a 1.6mm thick, symmetrical 4-layer stack with plane layers on layer 2 and 3 with 50 Ohm impedance structures on the top and bottom layers.
This will determine the height of both controlled impedance layers and require a "spacer" layer to pad the board to the specified thickness.
In this discussion all units are in millimeters.
<number>
© Polar Instruments 2010

## Slide 4: Virtual Material mode
In Virtual Material mode you use the Stackup Wizard to enter a few details about the stack, the number of layers, overall board thickness, plane layers, etc., along with solder mask and copper thickness. Speedstack will then build a stack to the specified board thickness by equally distributing the dielectric regions.
If a preferred core thickness is specified the software will maintain the dielectric thickness for core regions but then equally distribute prepreg regions to reach the target board thickness.
The target stack is shown overleaf.
<number>
© Polar Instruments 2010

## Slide 5: The target stackup
<number>
© Polar Instruments 2010
Target stack – 50 Ohm structures in top and bottom layers with spacer to achieve 1.6mm overall board thickness

## Slide 6: Using the Stack Wizard
Click the Select Symmetrical Mode button. From the Units menu choose Millimeters.
Begin in Virtual Material Mode (Tools|Virtual Material Mode); select File|New and choose the Stackup Wizard; fill in the Wizard's parameter fields as shown below.
<number>
© Polar Instruments 2010
Note especially the Board Thickness of 1.6mm and Plane Layers 2 and 3. Click Finish to display the stackup in the Stackup Editor.

## Slide 7: The initial generic stack
The Wizard produces an initial “generic” 4-layer stack with a height of 1.6mm.
As the preferred core height was specified at 0.2mm the Wizard creates the stack with equally distributed prepreg regions to reach the target board thickness.
The thickness is correct but now you need to add the controlled impedance structures, determining the height of the impedance layers and the resulting change in spacer height.
<number>
© Polar Instruments 2010

## Slide 8: Adding impedance structures
Add a 50 Ohm controlled impedance structure to determine Layer 1 height – the stack is symmetrical so Layer 1 will be reflected in Layer 4.
Ensure Symmetrical Mode is selected. Click on Layer 1 Foil in the stack and click the Controlled Impedance tab.
Click the Add New Structure button and choose the single-ended Coated Microstrip 1B structure with a target impedance of 50 Ohms (leave the tolerance at 10%). Click Apply then Done.
<number>
© Polar Instruments 2010

## Slide 9: Calculating the impedance of the structure
With the structure added, calculate the impedance of the structure:
For the parameters shown right the resulting impedance is 98.19 Ohms.
Next, calculate the Layer 1 height required for 50 Ohm impedance – keep the current trace widths and use Speedstack's Goal Seek, varying “H1 only” to achieve the 50 Ohm target.
<number>
© Polar Instruments 2010

## Slide 10: Goal seeking the impedance value
Click the Goal Seek button and choose the H1 Only option:
<number>
© Polar Instruments 2010
Speedstack calculates the substrate height required for a 50 Ohm structure

## Slide 11: Replacing with library materials
Click the alert (below) to display the new parameter value for H1 – 0.148 mm.
<number>
© Polar Instruments 2010
The 0.63 mm “virtual” substrate must be replaced with real materials that provide the 0.148mm dimension for H1, so switch to Material Library mode; from the Tools menu uncheck Virtual Material Mode.
Right click the Layer 1 prepreg and choose Swap to display the Material Library.

## Slide 12: Replacing with library materials
From the Materials Library choose Prepreg 1080 – 0.0762 thickness (two of these should get close to the target.)
<number>
© Polar Instruments 2010
Layer 1 prepreg is now 0.0762 thick – notice that with Speedstack in Symmetrical mode the bottom layer has also been updated.
Next, add another prepreg of the same thickness.

## Slide 13: Replacing with library materials
Right click Layer 1's PrePreg 1080 and choose Add|Prepreg; from the Material Library choose PrePreg 1080 and click the Add Material Above button.
The new stack reflects the added materials:
Next, recalculate the impedance with these new materials...
<number>
© Polar Instruments 2010

## Slide 14: Replacing with library materials
Rebuild and recalculate the stack with the new materials.
The structure's impedance now reads 50.9 Ohms.
Repeat the Goal Seek, this time adjusting the trace widths, i.e., goal seeking on parameters W1/W2 only (see Slide 10); the resulting impedance reads 49.78 Ohms.
The board thickness, though, has now reduced to 0.64 mm so the core must be padded to achieve the target 1.6mm board height.
<number>
© Polar Instruments 2010

## Slide 15: Restoring the overall stack thickness
To achieve the target stack thickness, you can specify a “manufacturer's spacer” to the core between layers 2 and 3. Note that you will only specify thickness – not actual materials.
Select the Tools menu and return to Virtual Material Mode; right click the Core and choose Properties – in the Description field supply narrative text, e.g., "Manufacturer Spacer" and change the Isolation Distance to 1.15mm.
<number>
© Polar Instruments 2010

## Slide 16: Restoring the overall stack thickness
Rebuild and recalculate the stack with the new core.
The completed stack is shown below:
Given the spacer dimensions the fabricator can build the spacer with appropriate available materials.
<number>
© Polar Instruments 2010

## Slide 17: Summary
Easy switching between Speedstack's Material Library and Virtual Material modes provides a powerful "freehand" approach to building and experimenting with stackups, allowing you to combine real and virtual materials in the same stack. The finished stackup technical report is shown on the next slide.
<number>
© Polar Instruments 2010

## Slide 18: Completed stackup technical report
<number>
© Polar Instruments 2010

## Slide 19: Thank you for using this presentation
<number>
This presentation is just one of a series of hands on tutorials designed to help you get the most out of your Si8000 and Si9000 Field Solvers, Speedstack stackup design system and CGen Coupon generator
Please view our other step-by-step presentations available on the Polar Instruments web site www.polarinstruments.com
© Polar Instruments 2010

## Slide 20
For more information:
Contact Polar now: Phone
USA / Canada / Mexico Ken Taylor ( 503) 356 5270
Asia / Pacific
Terence Chew +65 6873 7470
Japan
Terumitsu Tsuji +81 45 339 0155
UK / Europe Neil Chamberlain +44 23 9226 9113
Germany / Austria / Switzerland Hermann Reischer +43 7666 20041-0
www.polarinstruments.com