## Slide 1: Documenting HDI and sequential lamination builds with Speedflex HDI
Polar Instruments Application Note AP523
(revised for v 11.06)

## Slide 2: Documenting HDI / sequential lamination builds with Speedflex HDI
<number>
A powerful tool for creating and documenting flex-rigid PCB layer stackups, Speedflex HDI is equally powerful at documenting the press cycles in sequential lamination/HDI.
© Polar Instruments 2011
<number>

## Slide 3: Creating the target stack with the Stack Editor
Consider the target stack below – it will require three press cycles. Build and document the final stack in Speedflex Stack Editor and then use Speedflex Navigator’s Add Stack to document each press cycle, building up the stack in the Navigator. Each press cycle then appears as a separate stack in the Navigator.
© Polar Instruments 2011
<number>

## Slide 4: Using the Speedflex Navigator to add press cycles
Switch the Stack Editor to 2-D view and press F4 to open Speedflex’s Navigator
© Polar Instruments 2011
<number>

## Slide 5: Adding the stack press cycles – Press cycle 2
The initial (master) stack is shown in Speedflex Navigator. Use Navigator’s Add Stack to copy the stack, and create sub-stack Press cycle 2.
© Polar Instruments 2011
<number>

## Slide 6: Editing the press cycles – Press cycle 2
Select the sub-stack Press cycle 2 and use the Stack Editor to edit the stack. Add drills as required and select and disable the materials that are added in the final press cycle.
© Polar Instruments 2011
<number>

## Slide 7: Editing the press cycles – Press cycle 2
The new stack appears alongside the master stack; the process can be continued until the stack is complete, with as many press cycles as required – each shown as a separate stack in the Navigator.
© Polar Instruments 2011
<number>
Stack Editor
Navigator

## Slide 8: Moving stacks into sequence
© Polar Instruments 2011
<number>
Stacks can be moved left and right within the Navigator – right click the Press cycle 2 stack and move it left.

## Slide 9: Adding the stack press cycles – Press cycle 1
Stackup Editor
In the Navigator add another sub-stack, name it Press cycle 1 and use the Stack Editor to add drills and disable the materials as appropriate. In the Navigator move the new stack to the left.
© Polar Instruments 2011
<number>
Navigator

## Slide 10: The completed stack
The three press cycles are displayed left to right in Speedflex Navigator; the final stack will be reflected in the Technical Report.
© Polar Instruments 2011
<number>

## Slide 11: Speedflex HDI Technical Report
The Technical Report provides comprehensive high quality documentation
<number>
© Polar Instruments 2011

## Slide 12: Documenting HDI / Sequential lamination builds with Speedflex HDI
<number>
By using the multiple stack capability of Speedflex HDI fabricators and PCB specifiers can clearly document and share unambiguous information about HDI and sequential lamination process steps.
To learn more about how Speedflex HDI and Speedstack could enhance your documentation of high speed impedance controlled layer stackups, from simple 6 layer builds to the most complex HDI, flex-rigid and sequentially laminated PCBs please contact your local Polar office for a brief web introduction (recommended) or an evaluation licence. View a video introduction to Speedflex
Contact your local Polar office
© Polar Instruments 2011
<number>

## Slide 13
For more information:
Contact Polar now: Phone
USA / Canada / Mexico Ken Taylor ( 503) 356 5270
Asia / Pacific
Terence Chew +65 6873 7470
Japan
Terumitsu Tsuji +81 45 339 0155
UK / Europe Neil Chamberlain +44 23 9226 9113
Germany / Austria / Switzerland Hermann Reischer +43 7666 20041-0
www.polarinstruments.com