## Slide 1
Offset stripline - Construction matters
How the Si8000 and Si6000 approach calculating offset stripline impedance
www.polarinstruments.com Version I

## Slide 2
Question: Why does the Si8000 sometimes give an impedance value that is significantly different from that computed with the Si6000?
Answer: Because the you may have confused the dimensions and introduced an error. When introduced, the Si8000 dimension labeling became more rational. The layer dimensions now “count” up from the bottom of the diagram.
Given similar, correct input data, the two solvers correlate to within, typically, 0.1 ohm or better.
Si6000
Si8000

## Slide 3
Answer: The Offset Stripline 2B1A suggests that the construction is PrePreg, Core, PrePreg whereas the 1B2A suggests that the construction is Core, PrePreg, Core.
You may use the 1B1A structure for single PrePreg and single Core of course, or when either Er3 & Er2, OR Er2 & Er1 are the same (in which case they form an electrically homogenous dielectric.)
Question: Why are there so many (confusing) structures? With Offset Stripline, for example, when should I select 2B1A, 1B1A or 1B2A?

## Slide 4
5 Mil
5 Mil
5 Mil
In this stackup each of the dielectric laminate layers is 5 mils thick. However, the relative positioning of core and prepreg materials determine the position of the signal layers relative to the ground planes, and to each other.

## Slide 5
5 Mil
5 Mil
5 Mil
5 Mil
5 Mil
5 Mil
5 Mil
5 Mil
L1 1 Oz
L2 1 Oz
L3 1 Oz
L4 1 Oz
L5 1 Oz
L6 1 Oz
L7 1 Oz
L8 1 Oz
L9 1 Oz
PrePreg
PrePreg
PrePreg
PrePreg
Core
Core
Core
Core
…etc. for a 16 layer board.
This representation of part of a 16 layer stack suggests that L3 has the same spacing and characteristics as L6 (they are both offset striplines with apparently similar dimensions.) However, the following slides show that tracks in these two layers have very significant differences for impedance purposes.

## Slide 6: Offset stripline (sometimes called dual stripline)
PrePreg
PrePreg
Core
H3 = 5 Mil
1.2 mil
3.8 mil
10.0 mil
H2 = 5 Mil
H1 = 5 Mil
Si6000
Si8000
Signal tracks embed into the prepreg, closer to the nearest grounds

## Slide 7: Offset stripline (sometimes called dual stripline)
PrePreg
Core
Core
1.2 mil
H3=5 Mil
H3=5 Mil
H3=5 Mil
5.0 mil
8.8 mil
8.8 mil
5.0 mil
Si6000
Si8000
Signal tracks embed into the prepreg and are further from the nearest grounds

## Slide 8
This representation of part of a 16 layer stack offers the first suggestion that there is a significant difference between the characteristics of layers 3 and 6.
It now becomes clear that as layer 6 becomes embedded in the prepreg, it is closer to the adjacent ground plane than layer 3 to its adjacent ground plane. Note also the direction of etch taper. These dimensional differences make a significant difference to the resulting impedance values.
Use of the SB200 Stackup Builder will remove this source of errors automatically.

## Slide 9
The Si8000/SB200 combination conveniently selects the correct structure and orientates the trapezoid track correctly before computing the track width for the target impedance, thus avoiding operator error.

## Slide 10
Once again notice the automatic correct orientation of the trapezoid track by the SB200 enabling the Si8000 to compute the correct track dimensions.
Since the track in this case is closer to the nearest ground plane, its width must be reduced to 3.1/3.7 mils (from 4.0/4.6 mils) to maintain the 50 ohm target impedance.

## Slide 11
H3
H2
H1
The track is embedded in the laminate either up (the shaded track) or down (the solid track) according to which laminate is PP and which is core. Clearly, this changes the track-to-plane spacing and, hence, the impedance..

## Slide 12
Polar tools to assist in layer stackup: SB200a PCB Stackup design system

## Slide 13
Polar tools to assist in impedance prediction: Si8000m Controlled impedance design system

## Slide 14
For more information please visit: www.polarinstruments.com
©2005 Polar Instruments
Your contacts at Polar:
USA Software sales: Ken Taylor (503) 356 5270 USA Equipment sales: Richard Smith (650) 344 1416 UK / Europe: Neil Chamberlain +44 23 9226 9113 Germany Austria Switzerland: Hermann Reischer +43 7666 20041-0 Korea: J.S.Bae (008) 222-6442493
Asia / Pacific: Amit Bhardwaj +65 6873 7470