## Slide 1: Speedstack PCB Stackup Builder
Symmetrical Build slashes stackup creation time in half.

## Slide 2
In this session we build an 8-layer stack – we begin with 3 cores and then illustrate how to use symmetrical build.
Create a new empty stackup and add three cores…
Use the Speedstack Symmetrical Build to achieve dramatic reductions in stackup build time

## Slide 3: Switch to 2-D view
Click the 2-D button to switch to 2-D View
2-D button

## Slide 4: Adding layers symmetrically
To achieve the required dimensions we need to add some prepreg layers between cores.
We’ll work in the top half of the stack – the Speedstack Symmetrical Mode will add layers to the lower half of the stackup to maintain stack symmetry
We’ll begin by selecting layer 3
Select Layer 3
Switch to Symmetrical Mode

## Slide 5: Inserting prepreg layers…
Now we add a layer of prepreg above…
The prepreg layer is reflected in the structure below
Here’s the layer we added
And here’s the layer added by Speedstack

## Slide 6: Adding a second layer of prepreg…
Now we add another layer of prepreg… Speedstack adds another layer below to maintain symmetry
Here’s the new layer we added…
…and here’s the new layer added by Speedstack

## Slide 7: Add a prepreg layer to the top of the stack…
Next we add a layer of prepreg above L1 – Speedstack adds the corresponding layer below L6
Add another prepreg layer above L1…
…this layer is added to maintain symmetry

## Slide 8: Adding a foil layer…
Next, we add a foil layer… …which is mirrored below. (As part of the process we invert layer L8)…
Here’s the new foil layer we added
…and Speedstack maintains symmetry with this layer

## Slide 9: Adding a layer of soldermask…
…and in a single step we add a layer of LPI solder mask to both sides of the board
Here’s the LPI solder mask we added…
…and the LPI layer added by Speedstack

## Slide 10: Adding Ident layers
Ident layers (not part of electrical symmetry) are applied separately to each side of the board
Ident layers are added manually to each side

## Slide 11: Assigning ground planes…
With all the material in place we assign ground planes… we begin with layer L2 – it’s reflected in layer L7.
Now we assign layer L2 as ground plane
Speedstack mirrors the ground plane in L7

## Slide 12: Assigning more ground planes…
We repeat the process for the other ground plane layers…
We assign layer L4 as ground plane…
…and Speedstack matches it with layer L5

## Slide 13
For more information and assistance with updating:
Contact Polar now:
Phone: USA / Canada / Mexico Ken Taylor ( 503) 356 5270 Asia / Pacific Amit Bhardwaj +65 6873 7470 UK / Europe Neil Chamberlain +44 23 9226 9113
www.polarinstruments.com